USER MANUAL VOICE RECORDER AND MP3 PLAYER MILESTONE 311

Congratulations for purchasing the voice recorder and MP3 player “Milestone 311” of Bones Ltd., Switzerland.

“Milestone 311” was developed specifically to meet the requirements of blind and visually impaired people.  It is based on its predecessor “Milestone 310”.

We hope that this user manual facilitates your optimal daily use of “Milestone 311”.

Bones Ltd. Schweiz.

Table of contents

1.	Brief Overview of Milestone 311	4

1.1.	Three applications in one handy device	4

1.2.	Voice recorder with internal memory	4

1.3.	Voice recorder with a memory card	4

1.4.	MP3 player	4

1.5.	Data transfer between Milestone 311 and a computer	5

2.	Description of the device and its operational elements	5

3.	Summary of operation of all functions	6

4.	Detailed description of operation of all functions	8

4.1.	Selection of application and general device functions	8

4.1.1.	On/off (sleep mode)	8

4.1.2.	Selection of application	8

4.1.3.	Volume control	8

4.1.4.	Locking of keyboard	9

4.1.5.	Memory and battery status check	9

4.1.6.	Battery charging	10

4.1.7.	Use of headphones	10

4.1.8.	Use of external recording sources	10

4.2.	Voice recorder	11

4.2.1.	Main usage	11

4.2.2.	Recording	11

4.2.2.1.	Short recording	11

4.2.2.2.	Continuous recording	11

4.2.2.3.	Recording through line-in entrance	11

4.2.2.4.	Write protection of memory cards	12

4.2.2.5.	Technical details related to the recording function	12

4.2.3.	Playback	12

4.2.4.	Playback of previous or next message	13

4.2.5.	Jump to the first or last message within a folder	13

4.2.6.	Scrolling (navigating within a long message)	13

4.2.7.	Erasing messages	13

4.2.7.1.	Erasing one message	13

4.2.7.2.	Erasing all messages in a folder in one direction	14

4.2.7.3.	Erasing all messages within a folder	14

4.2.8.	Folder selection	14

4.2.9.	Voice labelling of folders	14

4.3.	Memory cards	15

4.3.1.	Main usage	15

4.3.2.	Useable memory cards	15

4.3.3.	Insertion and removal	15

4.4.	MP3 player	16

4.4.1.	Main usage	16

4.4.2.	Playback	16

4.4.3.	Navigation	16

4.4.3.1.	Navigation within a hierarchical level	17

4.4.3.2.	Navigation from one hierarchical level to another hierarchical level	17

4.4.3.3.	Observed folder sequence during navigation	17

4.4.4.	Voice labelling of folders	18

4.5.	Data transfer and data administration	18

4.5.1.	Connection to a computer	18

4.5.2.	Data administration	19

4.5.3.	Software upgrades	19

5.	Troubleshooting	20

5.1.	Nothing works anymore	20

5.2.	Reformat memory	21

6.	Additional information, warranty and support	22

7.	Care and maintenance	22

8.	Technical data	22

9.	Limitation of Liability	23

# Brief Overview of Milestone 311

## Three applications in one handy device

- “Voice recorder with internal memory”

- “Voice recorder with a memory card”

- MP3 player that plays back audio files in MP3 format from an inserted memory card

The two voice recording applications differ only in the type of memory used but not in their functionality.  The navigation function between folders and subfolders within the MP3 player is acoustically supported.  Milestone 311 may be used on its own or in connection with a computer.

## Voice recorder with internal memory

- Recording voice messages or other sounds with a total recording time of up to two hours

- The number of separate recordings within the two hour recording time is not restricted

- The basic functions recording, playback, erasing of messages, selection of folders, voice labelling of folders and navigation between and within messages is easily accessible through the five tactile pushbuttons on the front of the device and the “Selector” button on the face side of the device

## Voice recorder with a memory card

- Basic functionality and the operation of these functions are identical to the above described application “voice recorder with internal memory”

- Recording voice messages or other sounds with a total recording time of more than two hours

- Line-in recordings from external microphones and other audio devices

## MP3 player

- Playback of a audio files in MP3 format like music, voice recordings and talking books from an inserted memory card

- Acoustically supported navigation function enables the user to easily manoeuvre between folders and subfolders without losing track

- Each folder can additionally be voice labelled with a recorded title

## Data transfer between Milestone 311 and a computer

- Milestone 311 may be connected to a computer through the supplied USB cable

- Audio files in MP3 format can be transferred between Milestone 311 and a computer.  This allows simple exchange of audio files in MP3 format between people as well as creating data backups

# Description of the device and its operational elements

Milestone 311 comes in a credit card sized casing.  The edges of the casing are slightly rounded.

The device is operated through six pushbuttons.  Five tactile pushbuttons are located on the topside of the device and they are arranged in a cross-wise pattern.  The sixth pushbutton is located on the face side pointing away from the user.  If the device is held in the user’s right palm, the sixth pushbutton may easily be accessed and operated by the right index finger.  If one is looking at the device from above the sixth pushbutton is on the left side of the face side.

Image: Operational elements of the Milestone 311

The five pushbuttons on the topside are named:

- “Rec” button (top button with round indent the size of a pinhead)

- “Play” button (middle button which contains no symbol)

- “Rew” button or left arrow button (left button with embossed left arrow pattern)

- “FF” button or right arrow button (right button with embossed right arrow pattern)

- “Mode” button (bottom button with an embossed cross pattern)

The sixth pushbutton is called “Selector” and it is used to rotate between the three available applications “voice recorder with internal memory”, “voice recorder with a memory card” and “MP3 player”.

Additional elements to be found on the casing are:

- On the face side pointing away from the user: “Selector” button on the left, a USB connector in the middle, and the connection for the battery charger on the right.

- At the right end of the face side pointing towards the user: “headphone jack” (also called “line-in”).  This “headphone jack” additionally serves as the line-in entrance for recordings directly through a cable instead of recordings by microphone.

- On the long face side pointing to the right you find a 20 mm (0.79”) slot for SD/MMC memory cards or hardware extensions.

- On the left side of the keyboard in the corner pointing away from you: a small light emitting diode which serves as a signal lamp.  The speaker is located on the topside between the keyboard and the edge closest to you.  It can be felt through the 25 holes in the casing.

- A connection loop for optional attachment of a carrying cord is cut horizontally from left to right into the bottom of the casing close to the face side pointing towards you.

# Summary of operation of all functions

| Task | Operation | Acoustic feedback |
| --- | --- | --- |
| “On” from sleep mode | 1 x any pushbutton on topside | Application and current folder |
| Selection of application | 1 x “Selector” | Application and current folder |
| Increase volume | “Mode” + right arrow | “Up” or voice message |
| Decrease volume | “Mode” + left arrow | “Down” or voice message |
| Locking of keyboard | “Mode” + “Rec” | “Keyboard locked” |
| Unlocking of keyboard | “Mode” + “Rec” | “Keyboard active” |
| Memory status and battery check | 1 x “Mode” for 1.5 seconds | “Internal memory”/ “Memory card”, “...”, “... MB”,“...% available” “Battery fully charged” “Battery charged” “Please charge battery” “Charge battery urgently” |
| Battery charging | Connection of charger or USB cable | Long low pitched beep (begin charging) |
| Short recording | “Rec” (keep pressed down) | - |
| Start continuous recording | “Rec” + “Play” | Sound sequence “low pitched-high pitched” |
| End continuous recording | “Rec” | Sound sequence “high pitched-low pitched” |
| Selection of line-in entrance as recording source (only for “voice recorder with memory card” application) | “Selector” + “FF” + “Rew” | “Next recording from external source” |
| Playback | “Play” | - |
| Pause | “Play” | - |
| Playback next message | “FF” | - |
| Playback previous message | “Rew”, if within 3 seconds of start of playback | - |
| Playback same message from start | “Rew” (after the message has played for more than 3 seconds) | - |
| Jump to last message within a folder | “FF” + “Play” | - |
| Jump to first message within a folder | “Rew” + “Play” | - |
| Scroll forward | “FF” (keep depressed) | Interrupted playback |
| Scroll backward | “Rew” (keep depressed) | Interrupted playback |
| Erase one message | “Mode” + “Play | Short beep |
| Erase all messages forward | “Mode” + “Play” + “FF” | 2 beeps with time interval in between |
| Erase all messages backward | “Mode” + “Play” + “Rew” | 2 beeps with time interval in between |
| Folder selection | “Selector” + one pushbutton on topside | Current folder |
| Voice labelling of folder (voice recorder) | “Selector” + one pushbutton on topside (keep depressed) | Sound sequence “low pitched-high pitched” (begin of recording), sound sequence “high pitched-low pitched” (end of recording) |
| Voice labelling of folder (MP3 player) | “Selector” + “Rec” (keep depressed) | Sound sequence “low pitched-high pitched” (begin of recording), sound sequence “high pitched-low pitched” (end of recording) |
| Begin playback for MP3 player | “Play” | Playback of current MP3 file |

| MP3 navigation within a hierarchical level – left | “FF” | Folder name (if available) |
| --- | --- | --- |
| MP3 navigation within a hierarchical level – right | “Rew” | Folder name (if available) |
| MP3 navigation from one hierarchical level to another hierarchical level – down | “Mode” | Folder name (if available) otherwise playback of first MP3 file |
| MP3 navigation from one hierarchical level to another hierarchical level – up | “Rec” | Folder name (if available) |

# Detailed description of operation of all functions

## Selection of application and general device functions

### On/off (sleep mode)

Milestone 311 has no on/off switch.  After ten minutes of inactivity, the device will automatically go into sleep mode to conserve battery charge (as long as it is not connected to a power outlet or a powered USB cable).  The device will reactivate upon pressing of any of the five topside buttons.  It needs about a second to become functional.  Subsequently, recordings from sleep mode will start with a delay of about a second.  Further recordings will start immediately with the pressing of the “Rec” button.

### Selection of application

Pressing the “Selector” button rotates Milestone 311 between the three available applications “voice recorder with internal memory”, “voice recorder with memory card” and “MP3 player”.  The selected application and the active folder are announced with a pre-recorded message.  The selected application, active folder and active message are memorized when the device goes into sleep mode.  After reactivation the device returns to the same application, folder and message as it was before going to sleep.  The three applications are announced with “internal memory“, “memory card voice recorder” and “MP3 player“.

### Volume control

To increase the volume, keep the “Mode” button (bottom button with an embossed cross pattern) pressed, while additionally pressing down the right arrow button.  To decrease the volume, additionally push down the left arrow button.  With each push of the right or left arrow button, the volume changes by one level.  Overall, there are 12 volume levels available.  If the volume is changed during playback of a message, then playback continues at the adjusted volume level.  If the volume is changed during paused mode then the messages “Up” or “Down” are played at the adjusted volume level.  Reaching the maximum and minimum volume levels during paused mode is indicated by a beep.  Instead of pressing the arrow buttons multiple times, you may also keep them depressed continuously.  After approximately one second, the volume will start to change continuously in the chosen direction.

### Locking of keyboard

To lock the keyboard, keep the “Mode” button (bottom button with an embossed cross pattern) pressed, while simultaneously pressing the “Rec” button (top button with round indent the size of a pinhead).  By doing this, all functions of the device are disabled.  This is indicated by the message “Keyboard locked”.  To unlock the keyboard, press the same combination of buttons once again.  The device will acknowledge this with the message “Keyboard active”.

Attention: To conserve energy, the device will automatically go into sleep mode after ten minutes of inactivity.  The device will reactivate upon pressing of any of the five topside buttons.  Please note that this will not unlock the keyboard.

### Memory and battery status check

To check the memory and battery status, press the “Mode” button (bottom button with an embossed cross pattern) for at least 1.5 seconds.  Then, you will hear a message indicating the memory and battery status.  Battery status is indicated in one of four levels, they are: “Battery fully charged”, “Battery charged”, “Please charge battery” and “Charge battery urgently”.  Reaching the third level (“Please charge battery”) indicates that about 40% of battery charge is still available.  The memory status will tell you which memory and which folder are currently active and which portion of the active memory is still available for recording, e.g., “Memory card voice recorder, 3, 256 MB, 30% available”.

At stage four of the battery status (e.g., “Charge battery urgently”) recording is not allowed anymore to protect the already recorded messages.  Playback is still possible and the recorded messages are safeguarded.  Four very brief low pitched warning beeps sound after each played back message to alert the user to recharge the battery.  At stage four of the battery status no user settings such as volume, pauses or similar commands are retained upon going into sleep mode.  This again ensures safeguarding of the already recorded messages.  If stage four of the battery status is reached during a recording, the device will automatically terminate the recording and will announce the battery status.  The performed recording is saved correctly up to the point at which the battery status beeps were heard.

The built-in rechargeable high capacity battery allows approximately 10 hours of use with one full charge when recording through the internal microphone and playback over the headphones.  Actual power use varies with the exact use of the device.  The least amount of power is consumed during continuous recording through the internal microphone.  The most power is consumed for high volume playback over the built-in loudspeaker.

### Battery charging

The built-in battery may be charged by connecting Milestone 311 to the powered battery charger or by connection the device to a computer via the USB cable.  The connection for the battery charger is located on the right side of the face side pointing away from you. The connection for the USB cable is located in the middle of the same side.  Start of the recharging cycle is acknowledged by a long “low-pitched” beep a few seconds after chrging is initiated.  During charging, the red signal lamp flashes about every three seconds.  Please check the power supplies if the “low-pitched” beep is not heard after connecting the cable.  If using the charger verify that the wall outlet is carrying current, if using the USB cable check the computer.  A beep will also sound if the battery is already fully charged.  You may easily check for the latter by pressing the “Mode” button (bottom button with an embossed cross pattern) for 1.5 seconds.  You may recharge the battery of your Milestone 311 at any time.  The memory effect known from nickel-metal hydride batteries does not apply since this voice recorder contains a rechargeable lithium battery.  You may therefore recharge your Milestone 311 as often as you like to ensure sufficient availability of energy for your applications.  One charge cycle of a fully empty battery will take no more than four hours.  You are not required to unplug the charger at that point, since charging is automatically interrupted.

### Use of headphones

Recorded messages as well as music files may be listened to over the internal loudspeaker of the Milestone 311 or through external headphones.  For best results use headphones with impedance of 32 ohms. The headphone jack needs to be standard 3.5 mm.

### Use of external recording sources

Milestone 311 has two recording source options.  One may either employ the built-in microphone or use an external audio source connected to the line-in entrance to make high-quality recordings.  The line-in entrance is designed for direct connection to the headphone exit of audio devices such as CD players, radios, computers or tape players.  For best results set the headphone exit volume to low.  External microphones require a pre-amplifier to raise the signal to the required level.  Your Milestone 311 dealer will advise you about potential devices and suppliers.

## Voice recorder

### Main usage

The main usage for the “voice recorder with internal memory” is recording voice messages such as shopping lists, schedule information and addresses or other sounds with a total recording time of up to two hours.  The number of separate recordings within these two hours is not restricted.

The main usages for the “voice recorder with a memory card” are recording of voice messages or other sounds with a total recording time of more than two hours and line-in recordings from external microphones and other audio devices.

The basic functionality and the operation of these functions are identical for both applications.  For improved data handling in both applications the recorded messages are stored in one of five selectable folders.

### Recording

#### Short recording

To record messages, press the “Rec” button (top button with round indent the size of a pinhead) and keep it pressed while recording.  For best results, speak at a normal volume and hold the device at a distance of approximately 10 cm (4 inches) from your mouth.

Milestone 311 stores recorded messages in one of five selectable folders.  The folders carry the internal names M1 to M5.

Attention: If you do change the folder names via a computer the messages will not be accessible through the voice recorder application anymore.  Renaming of the folders will cut the link between messages and folders.  The messages however are not lost and may again be played back either by changing back the folder names to M1 to M5 or by using the MP3 player application of Milestone 311 to play MP3 files from any folders.

#### Continuous recording

As an alternative to having to keep a button pressed during a recording you may start a continuous recording.  Press the “Rec” button (top button with round indent the size of a pinhead) then press the “Play” button (middle button which contains no symbol).  The device will acknowledge the start of the continuous recording with the sound sequence “low pitched-high pitched”.  To terminate the continuous recording, briefly press the “Rec” button (top button with round indent the size of a pinhead) again.  The device will acknowledge the end of the continuous recording with the opposite sound sequence “high pitched-low pitched”.

#### Recording through line-in entrance

When using the application “voice recorder with a memory card“ recordings from external microphones and other audio sources may be made via the line-in entrance.  To select the line-in entrance as the source for the next recording press the “Selector” button and both arrow buttons.  Now you may perform either a short recording or a continuous recording.  After completion of the recording or if another button then the “Rec” button is pressed the line-in entrance selection is revoked and the next recording will again use the built-in microphone as the recording source.

#### Write protection of memory cards

Memory cards are equipped with a little switch for write/erase protection.  Milestone 311 recognizes and honors this setting.  If recording is attempted on a write protected memory card the message “Write protected” is played.  The built-in internal memory can not be write protected.

#### Technical details related to the recording function

Recordings on memory cards are performed in 192 kbps MP3 format.  This corresponds to excellent sound quality.  Regular voice recordings with the built-in microphone are performed with 24 kbps.  Recording resolution is always 16 bit at a sampling rate of 44.1 kHz (line-in) or 32 kHz (microphone).

If the memory is already full when attempting a recording or becomes full during a recording the message “Memory full” is played.  If the memory card is removed during a recording onto the memory card the message “No memory card” is played.

The integrity of a recorded message is not guaranteed if the memory card is removed during a recording.  In the worst case, the memory card will need to be reformatted and all stored messages will be lost.  The user is in any case advised to investigate the status of the memory card with the computer and a disc repair utility after reinsertion of the card into Milestone 311.

File names for recorded messages are assigned automatically by the device at the time of recording.  The first file is called “M001.mp3”.  “M” stands for message and the digits “001” are a continuous number.  The second message is called “M002.mp3”.  The device reassigns file names automatically to keep the logical file order if a recording is inserted between already existing messages.

Additional MP3 files may be played back just like any recorded message if the MP3 files have been transferred into the provided folders via the USB connection.  Order of play is alphabetical.

### Playback

To playback messages, press the “Play” button (middle button which contains no symbol).  The same button also has a pause function.  You may pause playback of a message by pressing the “Play” button again and you may resume seamless playback by pressing the same button once more.  When you reach the end of a message, the device will stop playback automatically.  Pressing the “Play” button at this time will replay the message once more from the start.

If you would like to play a message from the start, while it is already playing, simply press the left pushbutton after the message has already played for more than three second.  If you press the left pushbutton before the message has already played for more than three second then the push of the button will take you to the start of the previous message.

When you change the application or folder the device will memorize the current message and potential pauses and will return to the same position when reentering that folder.  This is true for all folders.

### Playback of previous or next message

Using “FF”/”Rew” will select the next/previous message and will play it automatically.  You may stop the replay at any time by pressing the “Play” button (middle button which contains no symbol).  With the “Rew” button or left arrow button (left button with embossed left arrow pattern) you jump to the start of the current message.  If you press the “Rew” button before the message has already played for more than three second then the push of the button will take you to the start of the previous message.  The jump happens as you let go of the button to distinguish this function from scrolling.  Pressing “Rew” or “FF” multiple times allows you to jump quickly between messages.

After reaching the last message no further jumping forward is possible.  If such a jump is attempted a beep will sound.  The same is true for backward jumps.

### Jump to the first or last message within a folder

To reach the first recorded message in a folder, press and hold down the left arrow button while simultaneously and quickly pressing the “Play” button (middle button which contains no symbol).  The first message will play.  The last recorded message in a folder is reached in a similar manner by pressing and holding down the right arrow button and briefly pressing the “Play” button.

### Scrolling (navigating within a long message)

To quickly navigate within a long message, keep the left or right arrow button pressed constantly.  Scrolling as known from CD players will start after approximately one second.  The scrolling speed will increase over time from about triple speed to a maximum speed which is about twenty-fold.

### Erasing messages

#### Erasing one message

Playback the message you would like to erase.  While the message is playing, press and hold down the “Mode” button (bottom button with an embossed cross pattern) and briefly press the “Play” button (middle button which contains no symbol).  The command will be executed as you let go of the buttons.  A short beep will sound as an acknowledgement.  A message may be erased while it is being replayed or up to 10 seconds after the replay has stopped.

#### Erasing all messages in a folder in one direction

Pressing the triple-button combination “Mode”-“Play”-“FF” or “Mode”-“Play”-“Rew” respectively will erase all messages in a given folder in one direction.  The triple-button combination needs to be pressed for two seconds.  Erasing will include the message on which the play cursor is positioned at the time the command is issued.  Two long beeps will sound as acknowledgement of the erasing procedure.  One at the start of erasing and the second one once erasing has been completed.

Attention: This function is only available in paused mode.  It may take a while to complete (a few seconds or even minutes) if a large number of messages or very long messages exist.

#### Erasing all messages within a folder

For safety reasons, a single function that erases all messages at once within the internal memory or a memory card has been omitted.  All messages within a folder may be erased if starting from the first message all messages are erased forward or if starting from the last message all messages are erased backwards.  Alternatively an entire folder or all messages within a folder may be erased via the computer connection.  The most efficient way for erasing an entire memory card is also via the computer connection.

### Folder selection

Within the voice recording applications Milestone 311 possesses five folders each on the internal memory and on inserted memory cards.  Each folder may be selected directly via a two-button combination.  For this purpose you need to keep the “Selector” button pressed and briefly press down on any of the five topside buttons. “Rec” for folder 1, “Rew” for folder 2, “Play” for folder 3, “FF” for folder 4 and “Mode” for folder 5.  Each time a folder is selected or if the active application is changed the folder name is announced with “1”, “2”, etc..

### Voice labelling of folders

To change the voice label of a folder the same two-button combination which is used to select the folder has to be kept pressed down for recording.  Recording starts after a safety interval of four seconds and ends when the buttons are released.  The device signals start of recording with the sound sequence “low pitched-high pitched” and end of recording with the sound sequence “high pitched-low pitched”.  This new voice label is heard the next time the folder is selected.

The recorded voice label is discarded if it is shorter than 0.5 seconds and the old voice label will remain.  A voice label may be changed at any time by recording a new one.  To completely remove a self recorded voice label and to restore the original label of “1” to “5” you need to delete the file “FOLDER.NAM” within the given folder via the computer.

## Memory cards

### Main usage

Memory cards are used for recording voice messages or other sounds with a total recording time of more than two hours and line-in recordings from external microphones and other audio devices.  Audio files in MP3 format which are transferred to Milestone 311 via computer are also mostly stored on memory cards.  Additionally memory cards allow simple exchange of audio files in MP3 format between people as well as creating data backups of MP3 files.

### Useable memory cards

All commercially available SD memory cards (“Secure Digital”) may be used in connection with Milestone 311.  These memory cards are already formatted and may be used within Milestone 311 without further preparation.  Alternatively, older MMC memory cards (“Multimedia Card”) may also be used. Please note that the MMC memory cards are more difficult to use since it is possible to incorrectly insert them in Milestone 311.

Memory size is measured in megabyte (MB).  About 1000 megabyte make up a gigabyte (GB).  Currently (Fall 2005) available memory card sizes are from 256 MB to 1 GB.  Maximum card size for Milestone 311 is currently 2 GB.

### Insertion and removal

Memory cards need to be inserted into the memory card slot on the side of the device.  In the correct orientation the contacts of the memory card face forward and upward to the keyboard of Milestone 311.  On SD cards the contacts are easy to locate by the large grooves next to them.  With MMC cards locating the contacts is more difficult because the grooves are very small.  SD cards, unlike MMC cards, may not be inserted incorrectly in Milestone 311 (except by use of force).  The card needs to be pushed in until only about 2 mm (0.1“) of it stick out.  This is also indicated by the engaging of the locking mechanism.  Pressing the memory card in even more disengages the locking mechanism and allows removal of the memory card.  After insertion the memory card is locked in place in order for it not to fall out during use.  Please beware that use of force or small shocks may disengage the locking mechanism and the card may be lost that way.  Insertion of a memory card into a running Milestone 311 and operational readiness of the memory card are acknowledged by the sound sequence “low pitched-high pitched”.  If functions requiring a memory card are selected while no operational memory card is inserted in Milestone 311 then the device will signal this with the message “No memory card”.  If Milestone 311 does not encounter the required formatting on a memory card the message “No file system. Please format through PC connection” is played.  Please refer to chapter 5 “Troubleshooting” for a description of the required steps.

SD memory cards are equipped with a little switch for write protection.  The switch is located on the long side of the card with the larger notch.  It can be moved up and down with a fingernail.  The distance which the switch moves is about 3 mm (0.1”).  Write protection is enabled when the switch is farthest away from the grooved section of the memory card.  If recording is attempted on a write protected memory card the voice message “Write protected” is played.

## MP3 player

### Main usage

The MP3 player plays back audio files in MP3 format like music, voice recordings and talking books from an inserted memory card. The acoustically supported navigation function enables the user to easily manoeuvre between folders and subfolders without losing track.  Each folder can additionally be voice labelled with a recorded title.  Generally the data structure with all desired folders will be composed on a computer and transferred to Milestone 311 via a USB connection.  Afterwards you may use Milestone 311 to move freely within this data structure, listen to MP3 files and add voice labels to the folders.

### Playback

To playback messages, press the “Play” button (middle button which contains no symbol).  The same button also has a pause function.  You may pause playback of a message by pressing the “Play” button again and you may resume seamless playback by pressing the same button once more.  Milestone 311 will automatically play all MP3 files within the selected folder.  After completion of playback the device will stop automatically and will return to the start of the first file within the folder.  At this point you may restart playback or navigate to a different folder.

If automatic continuation of playback across the entire folder structure is desired then each folder needs to contain a file called “AUTONEXT.YES”.  This file may be empty (with size zero).  Automatic traversing of entire folder structures especially makes sense when listening to newspapers which are structured by folders.  These structures are usually generated electronically and an “AUTONEXT.YES” file may as well be generated automatically for each folder.

### Navigation

Navigation within a hierarchical level is achieved with the “FF” and “Rew” buttons.  The “Rec” and “Mode” buttons are used to navigate from one hierarchical level to another hierarchical level.

#### Navigation within a hierarchical level

“FF”/”Rew” are used to select the next/previous file or the next/previous folder.  With the “Rew” button you jump to the start of the current message.  If you press the “Rew” button before the message has already played for more than three second then the push of the button will take you to the start of the previous message.

To reach the first recorded message in a folder or to reach the first subfolder within a folder, press and hold down the left arrow button while simultaneously and quickly pressing the “Play” button.  The last recorded message/last subfolder is reached in a similar manner by pressing and holding down the right arrow button and briefly pressing the “Play” button.

To quickly navigate within a long message, keep the left or right arrow button pressed constantly.  Scrolling as known from CD players will start after approximately one second.  The scrolling speed will increase over time from about triple speed to a maximum speed which is about twenty-fold.  Letting go of the arrow button will resume playback at regular speed.

#### Navigation from one hierarchical level to another hierarchical level

To enter a folder you need to press the “Mode” button while being positioned on the folder.  You will know that you are positioned on a folder because the message “Folder…” will play as you navigate onto the folder.  Pressing the “Mode” button while not being positioned on a folder will trigger a beep.  Pressing of the “Play” button will either enter a folder or replay the next available MP3 file.

Pressing of “Rec” will always take the user up one hierarchical level if such a level exists.  If the user is already on the highest level another beep will sound.

Change of a hierarchical level is announced with the sound sequence “high pitched-low pitched” when descending and “low pitched-high pitched” when ascending.

Folder names are announced with „Folder...“.  If the folder has been voice labelled then the recorded folder name will be played.  If no voice labelling exists the folder will be announced with the number that corresponds to position of the folder within the current folder.  Example: the fourth folder will be announced with “Folder 4”.  Numbering continues only up to folder 10.  If additional folders exist then they will only be announced with “Folder”.  File names are not announced acoustically.

#### Observed folder sequence during navigation

If you are using the same memory card for the two applications “voice recorder with a memory card” and “MP3 player” then in addition to the MP3 files which you transferred from the computer to the memory card you will also find the five folders from the “voice recorder with a memory card” application on the memory card.  These folders are named M1 to M5.  If you have generated additional folders on the memory card via computer then the MP3 player will access all existing folders in alphabetical order.  Example: you have created the folders “Beethoven”, “Haydn” and “Strauss” and you have not yet voice labelled them using Milestone 311.  The folders on the memory card will now be accessed in the following order: “Beethoven” as “Folder 1”, “Haydn” as “Folder 2”, “M1” to “M5” as “Folder3” to “Folder 7” and “Strauss” as “Folder 8”.  In order for you to keep track of the folders we recommend that you voice label them right after you disconnect Milestone 311 from the computer (see below).

You may create as deep a folder and subfolder structure as you like.  At the highest level (root directory) Microsoft’s data system limits the number of folders/files to 512.  Within subfolders the number of folders/files is not limited.  The sequence of play of folders and files is alphabetical with all folders played before the files.

### Voice labelling of folders

To change the voice label of a folder the two-button combination of “Selector” button and “Rec” button has to be kept pressed down for recording.  Recording starts after a safety interval of four seconds and ends when the buttons are released.  The device signals start of recording with the sound sequence “low pitched-high pitched” and end of recording with the sound sequence “high pitched-low pitched”.  This new voice label is heard the next time the folder is selected.

The recorded voice label is discarded if it is shorter than 0.5 seconds and the old voice label will remain.  A voice label may be changed at any time by recording a new one.  To completely remove a self recorded voice label and to restore the original label of “1” to “5” you need to delete the file “FOLDER.NAM” within the given folder via the computer.

## Data transfer and data administration

### Connection to a computer

To communicate with a computer Milestone 311 needs to be connected to a computer via the supplied USB cable.  No additional software drivers are required for Windows ME, Windows 2000 or Windows XP.  Set-up of the connection is signalled with the message “Connection activated”.  The memory corresponding to the selected application – internal memory or memory card – appears on the computer as an external drive.  After the connection has been established audio files in MP3 format may be transferred between Milestone 311 and the computer.  This allows simple exchange of audio files in MP3 format between people as well as creating data backups.  Milestone 311 may not be manipulated through its keyboard as long as the USB connection is active.  After completion of data exchange between Milestone 311 and computer Milestone 311 needs to be properly logged-off from the computer (“Remove external drive”) and the USB cable needs to be removed before Milestone 311 returns to the last active application.  Removal of the USB cable is acknowledged with the message “Connection deactivated”.

### Data administration

Data administration including set-up of data structures with all desired folders will be performed on a computer and transferred to Milestone 311 via a USB connection.  Voice labels for the folders on the other hand need to be recorded through Milestone 311.  The alphanumeric name which a folder carries from the computer’s point of view (e.g., “Documents”) does not necessarily have any connection with the additional voice label which you may give the same folder.  The voice label of the folder “Documents” is not changed by you changing the folder name from “Documents” to “My texts” via the computer.

To safeguard against inadvertent deletion of system files (beeps, settings) these files are stored in a hidden part of the memory and they are not accessible via the computer.  The settings for the playback cursor and volume settings, etc. are stored in the “MSAVE.DAT” file at the top level of the internal memory.  The file carries the attribute “not visible” but may be displayed by Windows.  If the “MSAVE.DAT” file is deleted all pause settings, current volume settings, etc. will be lost and the device will return to the default settings.  Next time Milestone 311 goes into sleep mode a new “MSAVE.DAT” file is created.

If there is no file system available on the internal memory (not formatted) the message “No file system. Please format through PC connection” is played upon start-up of the device.  Milestone 311 needs to be connected to a computer via the USB cable and needs to be formatted.  Please refer to chapter 5 “Troubleshooting” for a description of the required steps.

### Software upgrades

Software upgrades on Milestone 311 may be performed quickly in a straightforward fashion by transferring the file with the new software into a root directory of the Milestone 311.  Please see below for the required steps:

- Connect your Milestone 311 via USB cable to a computer

- Copy the file with the new software into a root directory (highest level directory in the internal memory or on the memory card)

- Properly log-off your Milestone 311 from the computer

- Remove the USB cable from your Milestone 311

Within the next 2-3 minutes Milestone 311 will update automatically.  The device will let you know what it is doing.  Simply wait until you hear the message „Software updated“.

# Troubleshooting

## Nothing works anymore

If you feel that your Milestone 311 is not functioning properly then it may be that the device is not powered, the device is in sleep mode, the keyboard is locked, the volume is set to low or the memory is full.  Please perform the following checks prior to contacting your sales representative:

Step 1:

Does the device have adequate power supply?  Connect your voice recorder to a power outlet and ensure that the charger is powered. Recharge the built-in battery for at least half an hour.

Step 2:

Is the device turned on?  Press any button for at least half a second.

Step 3:

Is the keyboard locked?  While keeping the “Mode” button (bottom button with an embossed cross pattern) pressed, press the “Rec” button (top button with round indent the size of a pinhead) briefly and listen for the response of the device:

- You hear the message “Keyboard active”: Keyboard was locked and is now unlocked.  Go directly to step 5.

- You hear the message “Keyboard locked”: Keyboard has now just been locked.  Press the same combination of buttons once more to unlock the keyboard. The device will play the message “Keyboard active”.  Go directly to step 5.

- You hear no message: The volume of the device is possibly turned down.  Keep the “Mode” button (bottom button with an embossed cross pattern) pressed while simultaneously pressing down the right arrow button for approximately five seconds.  Go to step 4.

Step 4:

Has the locking of the keyboard been activated at low volume?  Press the “Play” button (middle button which contains no symbol) to playback a message.

- You hear one beep or a recorded message: The keyboard was not locked.  Go directly to step 5.

- You hear no beep and no recorded message: Locking of the keyboard was possibly activated at low volume.  Please repeat the test once from step 3.

  - If you hear one beep or a recorded message, go directly to step 5.

  - If you do not hear any beeps or a recorded message, the device is not functioning properly.  Please contact your sales representative.

Step 5:

Is the memory of your device full?  Perform a test recording by pressing down on the “Rec” button (top button with round indent the size of a pinhead), speaking a message and releasing the “Rec” button.

- Press the “Play” button (middle button which contains no symbol) to hear the test recording.  If you hear the test recording, the device is fine and may be used without further complications.  If you do not hear the test recording, the device is not functioning properly.  Please contact your sales representative.

- At the beginning of the recording, you hear the message “Memory full”: The memory of your voice recorder is full or almost full.  Delete a message by replaying it and, at the same time, keeping the “Mode” button (bottom button with an embossed cross pattern) pressed while pressing the “Play” button (middle button which contains no symbol).  Try again to perform a test recording.  Should this not be possible again, then, your device is not functioning properly.  Please contact your sales representative.

## Reformat memory

If your Milestone 311 plays the message “No file system.  Please format through PC connection” or you would like to format the internal memory or a memory card then please see below for the required steps:

- Connect your Milestone 311 via USB cable to a computer

- Select your Milestone 311 and open a pop-up window with the right mouse button

- Chose “format”.  Ensure that formatting is performed using FAT (selection field within Windows).  If you can chose between FAT32 and FAT (without numbers), chose FAT.

- Properly log-off your Milestone 311 from the computer

- Remove the USB cable from your Milestone 311

Milestone 311 does not give any acoustic feedback to acknowledge formatting.

Memory cards must be formatted with the standard FAT16 or FAT32 data system.  Milestone 311 is optimized for FAT16.  With FAT32 Milestone 311 operates slightly slower than with FAT16.

# Additional information, warranty and support

Available warranty varies by country and is limited by applicable laws at time of purchase.  The product must be purchased from a manufacturer-licensed distributor in the country of main residence of the user.

All parts of a warranty are voided by inappropriate use, mechanical overload or opening of device.

Please contact your sales representative for any warranty related issues of your Milestone 311.

# Care and maintenance

Clean the device with a moist, but not wet duster.  Do not use any cleaning agents.

The user may not replace the built-in lithium battery.  Due to product reliability issues, only the manufacturer may perform replacement of the battery.

# Technical data

- Recording capacity: 120 minutes

- Frequency range speech: 150 Hz to 8 kHz, music: 40 Hz to 20 kHz

- Bit rate during recording over built-in microphone: 24 kbps

- Bit rate during recording through line-in entrance: 192 kbps

- Sampling rate during recording over built-in microphone: 32 kHz

- Sampling rate during recording through line-in entrance: 44.1 kHz

- Sample resolution during recording: 16 bit

- Bit rate for playback: 8 kbps to 320 kbps

- USB 1.1 connection (only for Windows ME, Windows 2000 and Windows XP)

- Memory card slot SD/MMC, maximum card size 2 GB

- Headphone jack: standard 3.5 mm

- Body made of impact-resistant plastic

- Measurements: 85 x 54 x 14 mm (3.35” x 2.13” x 0.55”)

- Weight: 49 grams (1.7 ounces)

- Built-in rechargeable lithium battery

- Maximum charge time: 4 hours

# Limitation of Liability

The Services are provided to you “AS IS,” without any representation or warranty, express or implied. Bones Ltd. assumes no liability whatsoever for loss of data, so you should make a backup copy of your data. Bones Ltd. IS NOT RESPONSIBLE FOR ANY SPECIAL, INDIRECT, OR CONSEQUENTIAL DAMAGES RESULTING FROM THE SERVICES/PRODUCTS. Bones Ltd. is not responsible for Covered Products that are lost or stolen while in Bones Ltd. possession. Bones Ltd. total liability for the Services/Products shall not exceed $30.

Bones Ltd.

02/06